## Slide 1: Brain Anatomy Inference with Differentiable MRI simulators
Razvan Marinescu
University of California, Santa Cruz

## Slide 2: The dream of Magnetic Resonance Imaging in Neuroimaging
See inside the brain, map and measure every neuron
  Like histology, but in-vivo!

## Slide 3: The dream of Magnetic Resonance Imaging
Detect sophisticated disease biomarkers at different scales
  High-level: subtle boundaries between structures, sub-structures, cortical layers, …
  Low-level: De-myelination, axonal degeneration,
  Detailed mapping of tumour macro-/micro-environments
  Direct, noise-free measures of functional activity

## Slide 4: Current MRI technology has multiple shortcomings
Tumor environment can be mapped, but only to some extent
Detection of cortical layers is difficult
3T scan of 14-year old female with seizures
Hard to achieve high SNR in fMRI
Very far from mapping individual neurons!

## Slide 5: Machine Learning can help reconstruct MRI scans and infer underlying anatomy and function
Recon from (undersampled) k-space
Estimation of quantitative T1/T2/PD maps
AUTOMAP (Zhu et al, Nature 2018)
Qiu et al, MRM, 2022
However, why reconstruct only T1/T2-weighted scans, or quantitative T1/T2 maps. Why not reconstruct entire digital brain phantoms?

## Slide 6: Achieving the MRI dream: digital brain phantoms
Aubert-Broche, IEEE TMI, 2006
A digital brain phantom ideally describes everything about the tissue anatomy, as well as cellular and molecular makeup
Deals with partial volume effects
  A voxel contains % of each class tissue
Can include:
  Cellular markers: myelination, packing density, % axons, % synapses, % glia, …
  Molecular markers: concentration of amyloid, tau, alpha-synuclein, …)
  Functional markers: metabolism levels, perhaps broken down by types of neurons (inhibitory/excitatory)
1 voxel

## Slide 7: How can we learn patient-specific digital phantoms?
We cannot do supervised learning because:
  we lack the phantoms themselves to train on
  patients have different combinations of scans and sequences available (e.g. T1-weighted with certain)
Solution: MRI scanning simulators

## Slide 8: How does an MRI simulator work?
Inputs: seq and PD/T1/T2 -> Output: e.g. T1-weighted
Forward simulation uses the underlying physics of the MRI magnetization

## Slide 9: How is the magnetization simulated at each voxel?
A single voxel’s state is represented as a matrix of F states:
RF rotation is modelled with a rotation matrix
Gradients are simulated by linear shifts:
  magnetization in Fn -> Fn+1
  Can also be written in matrix form
Precession is multiplication by a diagonal matrix:
We work with Extended Phase graphs:
A pulse sequence is therefore modelled as a multiplication of several matrices corresponding to precession, RF rotations and gradients => can make it differentiable
A recent simulator (MRZero) by Zeiss et al 2021 is differentiable by design

## Slide 10: Our contribution: once you have a differentiable simulator, how do you optimize a digital phantom?
Back-propagate the loss to the digital phantom
Inverse problem + ill-posed:
  Forward process is a projection of the phantom on some space
  Some MRI sequences are not sensitive to some tissues
loss
MRI simulator
Sequence params: TE, TR, flip angle, …
T1/T2/PD
simulated T1-weighted
% GM
% WM
% CSF
real T1-weighted
Digital phantom
K-space

## Slide 11: Results: we reconstructed patient-specific digital phantoms on the Brainweb dataset
This used 6 pulse sequences
Can do it with only 1 sequence also, but the problem becomes more ill-posed.

## Slide 12: What about Diffusion MRI?
Diffusion MRI simulators exist (e.g. Disimpy, SpinDoctor), but none are differentiable
We are currently building a PDE-based diffusion MRI simulator that is differentiable (in PyTorch)

## Slide 13: Part 2: Implicit representations

## Slide 14: A recent discovery: coordinate networks can learn implicit representations of scenes and perform efficient, real-time rendering
NERF, Mildenhall, 2020
Real-time NERF rendering on mobile devices (Rojas, 2023)

## Slide 15: Gaussian Splatting is a very recent technique for 3D scene reconstruction

## Slide 16: We built a Gaussian Splatting model for CT novel view synthesis
In CT we get projection views from multiple angles
Can we learn a Gaussian Splatting model from sparse-view CT?
  Equivalent in computer graphics: few viewing angles of a 3D scene.

## Slide 17: Results on Parkinson’s CT dataset (PPMI)
Gaussian Splatting (50% of views / 360) Standard ground truth (100%)
Ultra-low dose (10%)

## Slide 18: Future directions

## Slide 19: Extremely detailed, patient-specific digital brain phantoms
Derive phantoms for every subject in large brain datasets(ADNI, PPMI, AIBL)
Combine multiple modalities together: MRI, PET, CT, …

## Slide 20: Optimize MRI sequence to achieve downstream task
Task: e.g. Hippocampal subfields segmentation, AD detection
MRI simulator
Sequence params: TE, TR, flip angle, …
T1/T2/PD

## Slide 21: Compressed sensing using generative priors
Learn generative models (diffusion models) over the distribution of brain phantoms
Powerful compressed sensing using the generative model as a prior
=> Significant leap forward towards the MRI dream